# ISO/OSI Layer Model

## Layer

| Layer | Name | Examples | Remarks |
| --- | --- | --- | --- |
| 7 | Application | SMTP, NFS, HTTP, FTP, TELNET, DNS, SNMP, POP, IMAP, LDAP |  |
| 6 | Presentation | XDR |  |
| 5 | Session | RPC |  |
| 4 | Transport | TCP, UDP | TCP = connection oriented (reliable) UDP = connection less (fast) |
| 3 | Network | IP, ICMP, IGMP | IP-Address 32 Bit Fragmentation of big Packets MTU = ca. 1500 Bytes |
| 2 | Data Link | ARP, RARP, SLIP, PPP | MAC Address 48 Bit, Translation from MAC to IP via ARP |
| 1 | Physical | Ethernet, X.25 |  |

## Structure of TCP/IP Data Packages

| ARP Header | IP Header | TCP Header | Data |
| --- | --- | --- | --- |

Header Size = 28+ 24 + 24 = 76 Bytes

## Structure of UDP Data Packages

| ARP Header | IP Header | UDP Header | Data |
| --- | --- | --- | --- |

Header Size = 28+ 24 + 8 = 60 Bytes

## ARP Datagram (RFC 826)

Word 1-7 = Header (28 Bytes)

| Hardware Type | Protocol Type |
| --- | --- |
| Hardware Addr. Len = 6 | Protocol Addr. Len = 4 | Opcode |
| Source Hardware Address |  |
|  | Source Protocol Address, Part 1 |
| Source Protocol Address, Part 2 |  |
|  | Destination Hardware Address |
| Destination Protocol Address |
| Data |

## IP Datagram (RFC 791)

Word 1-6 = Header (24 Bytes)

| Version | IHL | Type of Service | Total Length |
| --- | --- | --- | --- |
| Identification | Flags | Fragment Offset |
| TTL = Time To Live | Transport Protocol | Header Checksum |
| Source Address |
| Destination Address |
| Options | Padding |
| Data |

## TCP Datagram (RFC 793)

Word 1-6 = Header (24 Bytes)

| Source Port | Destination Port |
| --- | --- |
| Sequence No. |
| Acknowledge No. |
| Header Length | Reserved | Flags | Frame Size |
| TCP Checksum | Priority |
| Options | Padding |
| Data |

## UDP Datagram (RFC 768)

Word 1-2 = Header (8 Bytes)

| Source Port | Destination Port |
| --- | --- |
| Total Length | UDP Checksum |
| Data |

## ICMP Datagram (RFC 792)

Word 1 = Header (4 Bytes)

e.g. used for “ping”

| Type | Code | Checksum |
| --- | --- | --- |
| Data |